## Slide 1: Free RTOS Practical Implementation
Real Time operating system

## Slide 2: Building Blocks of Free RTOS
Scheduler
Tasks
Mutex/Semaphores
Queues
ISRs

## Slide 3: Task Creation Define required Resources for the Task itself
Task Control Block
        StaticTask_t xLoggerTaskBuffer;
Task Pointer (void *)
        TaskHandle_t loggerTaskHandle;
Task Stack
        StackType_t xLoggerStack[MAJOR_STACK_SIZE]
Task Creation
        loggerTaskHandle =
        xTaskCreateStatic(st_LoggerTask, "LG", MAJOR_STACK_SIZE, NULL, G3_TASK_PRIORITY, xLoggerStack, &xLoggerTaskBuffer);

## Slide 4: Queue Creation
Queue Memory Block
        uint8_t loggerQueueStorageArea[mainQUEUE_LENGTH * QUE_MSG_SIZE]
Queue Handle
        QueueHandle_t LoggerQueue
Queue Control Structure
        StaticQueue_t xloggerQueueOHead
Queue Creation
        LoggerQueue = xQueueCreateStatic(mainQUEUE_LENGTH, QUE_MSG_SIZE, loggerQueueStorageArea, &xloggerQueueOHead);
        vQueueAddToRegistry(LoggerQueue, "Logger Queue");

## Slide 5: Semaphores & Mutexes
Semaphore Memory Block
        StaticSemaphore_t xTimeMutexBuffer;
Semaphore Handle
        SemaphoreHandle timeMutex
Semaphore Creation
        uiMutex = xSemaphoreCreateBinaryStatic( &xUiMutexBuffer )
        xSemaphoreGive(uiMutex)

## Slide 6: Starting a Free Rtose System
Initialize base hardware and HAL resources
Prepare all ISR resources
Call for the start of the scheduler
Scheduler will call freertose.c which will have all the tasks and their resources
Once all the tasks and resources are created the rtose will start running all tasks as designed

## Slide 7: vTask Delay
Allow Task function delay to wait on resources or create a periodic execution
Allows the Scheduler to do a context switch to allow other tasks to run
Managed by OS so if 10 msec is requested a minimum of 10 msec delay will be given.

## Slide 8: Task Structures
Can be coded as a finite state machine
  Coded to break function into manageable chunks based on the state of a resource
  Very useful for sequencal functions
Message handler
  Wait on received message (Queue)
  Service the request
  Return to sleep waiting on the next request
Periodic Function
  Screen Refresh routine
  Monitoring hardware resource (Magnetic sensor)